## Slide 1: Performance test and analysis of the developed emergency release system for liquefied hydrogen installed in loading systems
5th September, 2018
2018 CEC conference
*Akihiko Inomata (Kawasaki Heavy Industries Ltd. and Kobe University)
Tomoaki Umemura, Jun Kawaguchi (Kawasaki Heavy Industries Ltd.)
Tsutomu Kawai (Tokyo-Boeki engineering Co., Ltd.)
Yoshihiro Naruo, Yusuke Maru (Japan Aerospace Exploration Agency, JAXA)
Tetsuya Senda (Japan Ship Technology Research Association, JSTRA)
Minoru Takeda (Kobe University)

## Slide 2: Outline
Background
Pressure drop analysis for ERS
Measurement of atmospheric hydrogen concentration at disconnection of ERS
Simulation of hydrogen diffusion at ERS disconnection
Summary

## Slide 3: Outline
Background
Pressure drop analysis for ERS
Measurement of atmospheric hydrogen concentration at disconnection of ERS
Simulation of hydrogen diffusion at ERS disconnection
Summary

## Slide 4: COP21 (Paris Agreement)
Target of CO2 Reduction:
・Japan： “26% by 2030”
・Advanced Nations including Japan：
“80% by 2050”
Dec. 2015
1. Background
De-carbonation society
- shifted from Low-carbon -
Global temperature rise less than 1.5℃ at most effort, as well as２℃ target
Became effective after 4th, Nov. 2016
170 nations and countries signed
(as of 1st, Dec. 2017)

## Slide 5
Initiative by Global Companies Hydrogen Council
Composed of 39 leading companies from energy, transportation, manufacturing industry and trading sectors: 24 steering members (above photo + 3M, Bosch, China Energy, Great Wall Motor, JXTG and Weichai) and 15 associate members.
A global initiative advocates long term target to move to hydrogen utilizing new energy economy
With understanding of importance of hydrogen on energy transition, Hydrogen Council aims to create effective action plan with Governments and other stakeholders
1. Background

## Slide 6
Hydrogen Introduction Vision 2050 Hydrogen Council & McKinsey
Hydrogen market, 2.5 trillion dollars, creates 30 million employment allover the world
Responsible for 18% of energy and 20% of CO2 reduction
CO2 reduction of 6 billion t/year（50 billion t/year as of 2010 including feed stock)
Hydrogen power generation of 1,500TWh/year（recent 10 years Japan：about 1,000TWh/year, the world：about 22,000TWh/year）
Excessive renewable energy of 500TWh/year will be stored and utilized
1. Background

## Slide 7
Basic Hydrogen Strategy (Ministries cooperation Common scenario)
From HP. of Prime Minister's Office
Hydrogen is an option as important as renewable energies (R.E.)
Mass production from low cost sources: utilizing brown coal and foreign R.E. (Develop international liquefied hydrogen supply chain）
Promotion of fuel cell vehicles and hydrogen refueling stations
Commercialization of hydrogen power generation and mass consumption of hydrogen (hydrogen consumption 10 mill. t/year, Power generation capacity 30GW)
Leading to growth strategy to leveraged Tokyo Olympic Paralympic Games
On December 26, 2017, the Ministerial Council on Renewable Energy, Hydrogen and Related Issues held its second meeting and decided on a Basic Hydrogen Strategy to accomplish a world-leading hydrogen-based society
1. Background

## Slide 8
The Concept of CO2-free Hydrogen Chains
Stably supplying energy while suppressing CO2 emissions
Resourcing country (Australia)
Utilizing country (Japan)
1. Background
Hydrogen transport/storage
Hydrogen use
Hydrogen production
Combined cycle power generators etc.
Process uses
Semiconductor and solar battery manufacture
Oil refinement, desulfurization, etc.
Transport equipment
Hydrogen stations
Fuel cell vehicles, etc.
Hydrogen gas turbines
Fuel cells, etc.
Transport equipment
Electrical power plants
Liquefied hydrogen containers
Liquefied hydrogen storage tanks
Production of hydrogen at low costs from unutilized resources (brown coal) and/or abundant recyclable energy
CCS
(CO2 capture/storage)
CO2-free hydrogen
Affordable renewable energy
Liquefied hydrogen carrier
Liquefaction/ loading
Brown coal
JAXA
Loading arms
Fig.1 LH2 supply chain
Emergency Release System (ERS)

## Slide 9
World-first ERS for LH2
1. Background
Operation: 1) Open of the clamper, 2) Two valve bodies are separated, and 3) Springs at each side push each valve to shut the flow path.
Advantages: 1) It has no shaft to operate valves, which leads low heat ingress from the shaft. 2) Stable operation because of its simple structure. It is important when ERS is required to operate at the emergency case.
Disadvantage: 1) Relatively high pressure drop because of its narrow flow path. 2) Amount of diffused LH2 is relatively high at disconnection.
Fig.2 Concept of ERS for LH2

## Slide 10
Purpose of this study
Performance of Developed ERS
・It is important to assess the world-first ERS for LH2.
Especially,
- Pressure drop performance of check type valve
- performance of hydrogen diffusion at disconnection operation
This Study
Simulation on distribution of pressure drop and flow rate by CFD (Computational Fluid Dynamics).
Disconnection test of ERS prototype and measurement of diffused hydrogen concentration.
Simulation of hydrogen diffusion and comparison with experimental data.
1. Background

## Slide 11: Outline
Background
Pressure drop analysis for ERS
Measurement of atmospheric hydrogen concentration at disconnection of ERS
Simulation of hydrogen diffusion at ERS disconnection
Summary

## Slide 12
1) Simulation model for ERS
2. Pressure drop analysis
Table. Analysis conditions. | 
Application | FLUENT (version 17.2)
Steady/unsteady | Steady state
Adopted turbulence flow model | Realizable k-e model
Property of LH2 | Density: 70.8 [kg/m3] Viscosity coefficient: 1.33E-5 [Pa･s]
Flow rate at Inlet | 5.64 [m/s]
Pressure at outlet | 0 [PaG]
Fig.3 CFD Simulation model

## Slide 13
2) Calculation result of distribution of pressure drop
2. Pressure drop analysis
Overall pressure drop is 9.89E+3 Pa.
 Not serious value, because of physical property of LH2.
Some area are seemed to affect mainly.
Fig.4 Pressure distribution

## Slide 14
3) Calculation result of flow rate distribution
2. Pressure drop analysis
High speed area colored red affects large pressure drop.
 Shape, size, and location of springs and valve should be improved.
Fig.5 Flow rate distribution

## Slide 15: Outline
The Concept of CO2-free Hydrogen Chains
Pressure drop analysis for ERS
Measurement of atmospheric hydrogen concentration at disconnection of ERS
Simulation of hydrogen diffusion at ERS disconnection
Summary

## Slide 16
1) Layout of the test apparatus measuring diffused hydrogen concentration after disconnection
3. Measurement for diffusion
Test was conducted at JAXA (Japan Aerospace Exploration Agency) rocket test facility in Noshiro city in Japan.
ERS prototype was located vertically.
LH2 was supplied from top and bottom piping.
Boil off gas is disposed at vent stack through the piping.
After disconnection, ERS upper part goes up by cylinder vertically
Fig.6 Test apparatus

## Slide 17
Sensors are contact burning type. Range: 0 to 40000 ppm
The three axis ultra-sonic vane anemometer near the ERS
Direction from ERS to the tower was 230 degrees clockwise from the north.
2) Location of the tower of hydrogen concentration sensors
3. Measurement for diffusion
Fig.7 Location of sensors

## Slide 18
Time recorded peak concentration is 4.5 to 5s at each sensor.
There are some small peaks after 5s.
Peak value of No.4 is the biggest and No.6 is the smallest of the three.
Fig.8 Measurement result for sensor No.4, 5, and 6.
3) Test results of concentration
3. Measurement for diffusion

## Slide 19
Fig.9 Measurement result on wind’s clockwise angle from the north.
4) Measured wind direction value
3. Measurement for diffusion
Mean value was 214 degrees from the north, therefore wind direction was 16 degrees anticlockwise of the sensor tower from ERS.
It is reasonable that peak value of No.4 is the biggest and No.6 is the smallest of the three.
ERS Prototype
Wind direction

## Slide 20: Outline
The Concept of CO2-free Hydrogen Chains
Pressure drop analysis for ERS
Measurement of atmospheric hydrogen concentration at disconnection of ERS
Simulation of hydrogen diffusion at ERS disconnection
Summary

## Slide 21
1) Outline of the software “Phast”
4. Simulation of hydrogen diffusion
Developed by DNV, improved for 30 years, and has validated for hydrogen.
Basically based on Pasquill’s equation that concentration distribution is expressed by Gaussian distribution as below.
The model of dispersion of the plume is included movement and vaporization of drops of liquefied gas.
Heat exchange between atmosphere and plume considering change of temperature and phase.
Atmospheric stability proposed by Pasquill and the density of the plume also affect values on distribution.
f(z) can be expressed as well.
Where C is gas concentration at any x point [volume fraction], Q is flow rate of dispersed fluid [m3/s], u is wind speed along x axis [m/s], sy, sz [m] are standard deviation for gas concentration at y and z axis direction respectively.

## Slide 22
2) Calculated concentration contour figure
With the lapse of time, gas plume is diffusing moving to the downstream.
1s after the dispersion, the area within explosion range is observed, while 5s after the dispersion, explosion concentration is disappeared.
1s after the dispersion
5s after the dispersion
10s after the dispersion
4. Simulation of hydrogen diffusion
Fig.10 Hydrogen concentration contour

## Slide 23
3) Comparison simulation with experiment
Measured peak mountain is broader than calculated one.  Supposed effect of change of wind speed and maintained liquid on ERS lower part.
Measured peak value is more uniform than calculated one.  Supposed effect of change of wind direction
ERS Prototype
Wind direction
4. Simulation of hydrogen diffusion
Fig.11 Measured and calculated concentration

## Slide 24: Outline
Background
Pressure drop analysis for ERS
Measurement of atmospheric hydrogen concentration at disconnection of ERS
Simulation of hydrogen diffusion at ERS disconnection
Summary

## Slide 25
Established Technical Research Association
Name of TRA: CO2-free Hydrogen Energy Supply-chain Technical Research Association (Abbreviation: HySTRA)
Established date: February 2016
Member: KHI, Iwatani Corporation, Shell Japan, J-Power (as of established date)
NEDO “Demonstration project for establishment of mass hydrogen marine transportation supply chain derived from unused brown coal”
New Energy and Industrial Technology Development Organization (NEDO);
Development of Technologies for Realizing a Hydrogen Society, Development of Technologies for Large-Scale Hydrogen Systems,
Demonstration project for establishment of mass hydrogen marine transportation supply chain derived from unused brown coal
5. Summary
Fig.12 Demonstration project conducted from 2015 to 2020

## Slide 26
5. Summary
5. Summary
Performance of world-first ERS for LH2 was simulated and measured. We obtained knowledge as follows;
Pressure drop is estimated practical value, abt. 10kPa.
Flow rate distribution is also simulated and obtained data to be improved for the future ERS.
Diffusion of hydrogen at disconnection of ERS is measured and obtained the reasonable data.
Simulation can predict the concentration distribution of hydrogen very well
These method shall contribute future commercialization of LH2 supply chain and de-carbonation society.

## Slide 27
Acknowledgments:
A part of this work was supported by Council for Science, Technology and Innovation (CSTI), Cross-ministerial Strategic Innovation Promotion Program (SIP), “Energy Carriers” (Funding agency: JST).
Thank you for listening
Kawasaki, working as one for the good of the planet